## Slide 1
Radio over Fiber (RoF)
Technology, Architecture, Advantages, Applications and Limitations

## Slide 2
Agenda
1. What is Radio over Fiber?
2. How it works: architecture and building blocks
3. Analog vs. digital RoF
4. Advantages of RoF
5. RoF in Distributed Antenna Systems (DAS)
6. Application areas
7. Limitations, challenges and outlook

## Slide 3
Radio over Fiber: Definition & Principle of Operation
• Core concept: RoF transports an analog RF or IF waveform directly over an optical fiber carrier, rather than baseband digital bits.
• Downlink (E/O → O/E): at the central station, the RF/IF signal modulates a CW laser carrier (direct modulation or an external MZM). At the remote unit, a photodiode recovers the RF/IF signal for filtering, amplification and antenna transmission.
• Uplink: follows the reverse conversion path, from the remote antenna back to the central processing unit.
• Multiplexing: wavelength-division multiplexing (WDM) lets several RF channels share one fiber on different wavelengths (λ1 … λn).
Critical distinction: RoF removes the transport bottleneck, but it does not create extra radio spectrum or wireless air-interface capacity by itself.

## Slide 4
RoF Network Architecture
BBU: Baseband Unit · BS: Base Station · RRH: Remote Radio Head

## Slide 5
RoF Link Block Diagram
CW laser: continuous-wave source that provides the optical carrier.
MZM: Mach-Zehnder modulator; varies light intensity with the RF signal (alternative: direct laser modulation).
WDM MUX / DEMUX: combine and separate channels λ1 … λn when they share one fiber.
Photodiode: converts light back into the electrical RF signal at the base station (remote antenna site).
Filter and PA: remove out-of-band products and amplify the RF signal before the antenna.
Downlink shown; the uplink follows the reverse conversion path.

## Slide 6
RoF Remote Antenna Unit (RAU) Types
BBoF — baseband over fiber
RAU: modulator + mixer + LO. Converts baseband up to RF.
IFoF — intermediate frequency over fiber
RAU: mixer + LO. Converts IF up to RF.
RFoF — RF over fiber
RAU: photodiode + TIA + PA. No frequency conversion; simplest RAU.
All types
Downlink: photodiode, TIA, PA. Uplink: LNA, laser diode (LD).
TIA: transimpedance amplifier · PA: power amplifier · LNA: low-noise amplifier. Figure adapted from “Radio over Fiber: An Alternative Broadband Network Technology for IoT,” Electronics 9(11), 1785 (2020), Fig. 3.
Notes: Figure source: “Radio over Fiber: An Alternative Broadband Network Technology for IoT,” Electronics 9(11), 1785 (2020), Figure 3. DOI: https://doi.org/10.3390/electronics9111785.

## Slide 7
Analog vs. Digital RoF
Aspect | Analog RoF (A-RoF) | Digital RoF (D-RoF)
Signal on fiber | The RF waveform itself modulates the light | Sampled and quantized digital bits
Remote unit | Very simple: photodiode, filter, amplifier | More complex: needs DAC / ADC
Fiber bandwidth | Efficient | Very high; grows with antennas and bandwidth
Main weakness | Noise, nonlinearity, dispersion | High data rate, remote-unit cost and power
Standards | ITU-T G.9803 defines RoF system requirements, including IMT-2020 fronthaul in Amendment 2 (2022). | CPRI / eCPRI: digital fronthaul interface families.
Sources: Li et al. (2021); ITU-T G.9803 (2018), Amendment 2 (2022).

## Slide 8
Key Engineering Advantages of RoF
1. Ultra-low attenuation & extended reach
≈ 0.2 dB/km at 1550 nm (ITU-T G.652 SMF), so one central site can serve a wide coverage area. Reach is bounded by noise, nonlinearity and dispersion.
2. Large transport bandwidth
High fiber capacity, extended with WDM, supports multiple channels and operators on one fiber.
3. EMI immunity
The optical fiber span is immune to electromagnetic interference. Over-the-air RF interference still applies.
4. Centralized processing, low field maintenance
Complex processing stays at the BBU pool. Simpler remote units with fewer active parts reduce remote power and maintenance.
5. Protocol & modulation transparency
A transparent optical link carries multiple radio generations and modulation formats without changing remote hardware.
6. Cost & installation efficiency
Light, flexible cable simplifies installation in tunnels and buildings; existing dark fiber can be reused.
Note: wireless capacity remains governed by radio spectrum, modulation efficiency and the number of radio units, not by fiber bandwidth alone.
Fiber attenuation: typical single-mode fiber at 1550 nm, ITU-T G.652 family.